## Slide 1
Welcome to the Arduino Programming Workshop!
Date
5th May 2025
Presenter
Aman Sonwani
Sintu Hazarika
Rohit Kumar

## Slide 2
What We’ll Cover Today
Arduino Basics
What is an Arduino?
Setup
Installing Arduino software
Programming
Writing your first program
Project
Example uses and sketches
1
2
3
4

## Slide 3
Introduction to Arduino
Open-source Platform
Hardware and software combined
Beginner Friendly
Large supportive community
Variety
Arduino Mega , Arduino UNO , ESP32 etc.

## Slide 4
Download
From arduino.cc, free software
Connect
Arduino to computer via USB
Configure
Select board and correct port
Getting started with Arduino
& Arduino IDE

## Slide 5
Your First Arduino Sketch
setup()
Runs once at start
loop()
Runs repeatedly
Setup the connections.
Assign Pin to Connections using PinMode()
Function.
Assign other components to control variables.
Runs the commands and generate outputs.
Runs multiple times as a loop to generate
Output number of times.
Runs multiple times as a loop to generate
Output number of times.

## Slide 6
Demo: Blinking LED
Goal
Turn Led ON and OFF using arduino
Materials
Arduino, LED, breadboard, wires
Steps
Build circuit and upload code

## Slide 7
Functions used while programming
pinMode
Sets pin as output
digitalWrite
Turns LED on/off
delay
Pauses for 1 second

## Slide 8
Do the connections & Code
1
LED
Connect the LED’s anode (longer leg) to Arduino pin 9.
Connect the LED’s cathode (shorter leg) to GND on the Arduino.
Power: Connect the Arduino to your computer via a USB cable.
2
Steps to run
Open the Arduino IDE.
Copy and paste the code above into a new sketch.
Connect your Arduino to your computer.
In the IDE, go to Tools > Board and select your board (e.g., Arduino Uno).
Go to Tools > Port and select the correct port.
Click the Upload button (right arrow) to upload the code.
The LED on pin 9 should start blinking (on for 1 second, off for 1 second).

## Slide 9
Code for LED Blinking